SNO-STR-2001-12

Spectroscopic Investigation of Ferrous, Ferric, and Manganese Ions

in Aqueous Solution

Minfang Yeh and Richard L. Hahn

Department of Chemistry, Brookhaven National Laboratory

The impurities of iron and manganese in the SNO water are spectroscopically studied to understand their possible absorption between the wavelengths of 300 and 450 nm. The 2+ and 3+ oxidation states of iron are stable over broad regions of potentials and pH. Ferric ion can be reduced by hydrogen, while ferrous ions is slowly oxidized by air. The Fe2+ and Mn2+ ions show no absorption in the range of 300 to 450 nm. Thus the investigation concentrates on the absorption of ferric ions at different wavelengths.

The hydrolysis of ferric ions in aqueous solutions is a complicated time-dependent system. It can be defined as hydrolysis-polymerization-precipitation. A simple mechanism describes the process into several steps: (a) primary hydrolysis giving rise to low-molecular-weight complexes (mono- and dimer), i.e., Fe(OH)2+, Fe(OH)2+, Fe2(OH)24+; (b) formation and aging of polynuclear polymers, i.e., Fen(OH)m(H2O)x(3n-m)+ or FenOm(OH)x(3n-2m-x)+; (c) precipitation of ferric oxides and hydroxides, i.e., Fe(OH)3, FeOOH, and Fe2O3. The whole process from hydrolysis to precipitation can take several years.

At pH < 7, the dominant species of ferric solution are Fe(OH)2+, Fe(OH)2+, Fe2(OH)24+, Fe(OH)3, FeO(OH) and FeCl2+. Their equilibrium constants and molar absorptivities have been determined by several authors and are reported in Table 1.

In this study, UV/visible spectra of ferric ions in 0.2% NaCl solution (7.5 ( 10-5, 5 ( 10-5, 2.5 ( 10-5, and 1 ( 10-5 M) were measured in the region of 260 to 450 nm, respectively. The measured pH values in these solutions were in the range of 5.5 to 6.5. The measured values are shown in Table 2. It should be noted that the absorbance at each measured wavelength obeys Beer’s Law (Figure 1). A plot of mean molar absorptivity versus wavelength is also shown in Figure 2.

Table 1. Literature values of molar absorptivities and equilibrium constants of ferric species at various wavelengths

|  | ( (M-1.cm-1) | K |
| --- | --- | --- |
| ( (nm) | 290 | 300 | 310 | 320 | 330 | 340 | 350 | 360 | 370 | 380 |  |
| Fe3+ | 315 | 180 | 90 | 30 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| Fe(OH)2+ | 2005 | 2030 | 1850 | 1535 | 1175 | 835 | 560 | 335 | 210 | 120 | 2.7 (10-3 |
| Fe(OH)2+ | 1720 | 1745 | 1585 | 1253 | 853 | 760 | 615 | 535 | 480 | 455 | 1.3 (10-8 |
| Fe(OH)3 | - | - | - | - | - | - | - | - | - | - | < 10-12 |
| Fe2(OH)24+ | 2930 | 2053 | 2200 | 3760 | 5053 | 5095 | 4106 | 2080 | 1335 | 1065 | 6 (10-4 |
| FeCl2+ |  |  |  |  | 1420* |  |  |  |  |  | 5.2 |

*(max

Table 2. Mean molar absorptivities for ferric ions in 0.2% NaCl solution

|  | ( (M-1.cm-1) |
| --- | --- |
| ( (nm) | 260 | 270 | 280 | 290 | 300 | 310 | 330 | 350 | 360 | 380 | 400 | 450 |
| ( (M-1.cm-1) | 2629 | 2606 | 2590 | 2551 | 2451 | 2320 | 2053 | 1759 | 1559 | 1159 | 820 | 390 |

Since the Fe(OH)3 and FeO(OH) are solids, it is assumed that under equilibrium, they will have gradually descended to the bottom of container and will not contribute to the absorption caused by the solution. The ferric species in the aqueous solution are then dominated by the following reactions, the strengths of which vary with pH:

Fe3+ + H2O ( Fe(OH)2+ + H+		(1)

Fe3+ + 2H2O ( Fe(OH)2+ + 2H+		(2)

2Fe3+ + 2H2O ( Fe2(OH)24+ + 2H+	(3)

Fe3+ + Cl- ( Fe(Cl)2+			(4)

Without considering individual species, but using mean molar absorptivity from Table 2, the absorbance (A) and transmittance (T) at each wavelength for 4 ppb ferric ions (7.1 ( 10-8 M) were calculated with 1-cm pathlength or at 8 m from the center of AV, along with the attenuation length (L) at T=1/e. The results are shown in Table 3. The value of 4 ppb is the quoted concentration of iron in the D2O-NaCl solution in the AV, which is determined by ICP-MS that measures total iron, not different chemical forms of iron.

Table 3. The calculated absorbance (A) and transmittance (T) at each wavelength for 4 ppb

ferric ions at different distances from the center of AV

|  | 1-cm Cell | 8 m | Distance to 1/e |
| --- | --- | --- | --- |
| nm | A | A | T (%) | L (m) |
| 450 | 2.79E-05 | 0.022 | 95 | 156 |
| 400 | 5.86E-05 | 0.047 | 90 | 74 |
| 380 | 8.28E-05 | 0.066 | 86 | 52 |
| 360 | 1.11E-04 | 0.089 | 81 | 39 |
| 350 | 1.26E-04 | 0.101 | 79 | 35 |
| 330 | 1.47E-04 | 0.117 | 76 | 30 |
| 310 | 1.66E-04 | 0.133 | 74 | 26 |
| 300 | 1.75E-04 | 0.140 | 72 | 25 |
| 290 | 1.82E-04 | 0.146 | 71 | 24 |
| 280 | 1.85E-04 | 0.148 | 71 | 23 |
| 270 | 1.86E-04 | 0.149 | 71 | 23 |
| 260 | 1.88E-04 | 0.150 | 71 | 23 |

Note that after the addition of salt, the iron concentration in the SNO water was increased from few tenths of ppb to 4 ppb. This study shows that chloride ligand does not have a strong complexation effect with ferric ions and in the aqueous solution, the dominant species are ferric hydrolysis products, which can absorb the light from 450 to 260 nm, while ferrous and manganese ions show no indication of attenuation over the same region.

The calculated data presented in Table 3 are on the basis of 7.1 ( 10-8 M of ferric ions showing that 10% to 28% of the light in the wavelength range of 400 to 300 nm produced at the center of AV do not reach the PMT’s. However, the iron that exists in the SNO water can be a mixture of many different chemical forms, such as ferrous ions that have no absorption in the UV/visible region, or ferric and ferrous colloids that are not big enough to scatter the photons. It’s also conceivable that the ferric ions in the SNO water might be complexed with some unknown ligands that are present in the water holding the ferric ions in the aqueous phase, but not having any absorption in the optical region of interest. These possibilities indicate that the calculations from this study can only represent an upper limit on the possible absorption of light by iron in the SNO water.

It should be known that although the effect of iron impurities on the optical clarity of the D2O-NaCl solution has been shown in this work, we couldn’t distinguish how large the effect is without having actual samples taken from the AV for the spectroscopic analysis. We also cannot rule out other deleterious effects, besides iron chemical impurities, on optical clarity, such as coatings, chemical or biological, on the surface of the AV, or the degradation of the PMT’s glass.

# Text boxes

Figure 1. Beer’s law for ferric ions in 0.2% NaCl at different wavelengths. Different makers represent different wavelengths in Table 2 and some selected fittings are shown.

Figure 2. Mean molar absorptivity of ferric ions in 0.2% NaCl as a function of wavelength.

260 nm

360 nm

450 nm